## Slide 1
Ronglong Wu(吴镕龙), Shuyue Zhou, Jiahao Lu, Zhirong Shen, Zikang Xu,
Jiwu Shu, Kunlin Yang, Feilong Lin, and Yiming Zhang
Removing Obstacles before Breaking Through the Memory Wall:
A Close Look at HBM Errors in the Field
26th ACM SIGOPS Chinasys Workshop
Notes: Hello everyone, I'm Ronglong Wu from Xiamen University.
Today, I'd like to share with you our recent work,
“Mitigating Write Disturbance in Non-Volatile Memory via Coupling Machine Learning with Out-of-Place Updates”,
which focuses on the write disturbance problem, a prevalent issue in non-volatile memory.

## Slide 2
Outline
Background
Analyses and Findings
Calchas: Hierarchical Prediction Framework
Conclusion
Notes: I will introduce our work from these four parts.

## Slide 3
  Memory wall
Background: Memory Wall
The gap between computing power and memory bandwidth is continuously widening in modern systems[1]
  Processors are improving exponentially, but memory bandwidth is increasing slowly
[1] Micron Inc., Micron’s Perspective on Impact of CXL on DRAM Bit Growth Rate
  Processor performance
  Memory performance
  Performance
  Memory wall becomes one of the major obstacles in training LLM models.

## Slide 4
Background: High-Bandwidth Memory
  Save massive physical space by stack vertically
  Offer significantly higher data transfer rates
  Introduce reduced power consumption
HBM is a hopeful technology to overcome the memory wall
Die
Buffer die
TSVs
SID0
SID1
Each pseudo channel can be accessed independently

## Slide 5
Background: HBM Errors
Disadvantages of HBM Memory
  Packed within a DSA devices → Less flexibility
  Complex manufacturing process → More special
  Equip weaker ECC → More errors
  Errors in HBM are more common and distinct compared to DRAM, but there is a lack of analysis on HBM errors in real production environments.
NVIDIA A100 GPU[2]
Example of various micro-bump joint failures in HBM[3]
[2] NVIDIA A100 Tensor Core GPU. https://www.nvidia.com/en-us/data-center/a100/.
[3] Jun et al. HBM (High Bandwidth Memory) DRAM Technology and Architecture. Proc. of IMW, 2017.
HBM

## Slide 6
Outline
Background
Analyses and Findings
Calchas: Hierarchical Prediction Framework
Conclusion
Notes: I will introduce our work from these four parts.

## Slide 7
Analyses: Our Dataset
Over 15K DSA devices
  60K+ HBM2 memory chips
  460M+ errors
  19 data centers: diverse services
Test dataset released
Two years BMC log
  ErrLog_Cycle log: concise but fully recordable
  ErrLog_Occurrence log: detailed but difficult to fully retain
  Sensor log: temperature, power, etc.
  https://github.com/wrl297/Calchas

## Slide 8
Analyses: Hierarchical Levels
Errors in different positions
  Root cause: The effects of crosstalk in the HBM may result in data loss
E.g., A BankGroup consists of four Banks, each located in different positions. Count the number of errors at each different bank position.
Finding: Errors occurring in the 7th, 15th, 23rd, and 31st columns are 338.4% higher on average than the errors in other column positions.

## Slide 9
Analyses: Hierarchical Levels
Errors in different positions
  Finding: Lower SIDs (i.e., SID1) exhibit a higher susceptibility to errors due to the due to poor heat dissipation in the lower SID
Top
Bottom

## Slide 10
Col-related modes (29.22%)
Row-related modes (5.0%)
Analyses: Error Modes
Typical error modes in a bank
Single-row
Two-row
Row-dominant
Single-col
Two-col
Col-dominant
  Column-related modes are more commonly observed in HBM, as opposed to the prevalent row-related modes in DRAM

## Slide 11
Analyses: Time between Errors
UER
CE
No error
Next
UER
First CE
Time
UER
Last CE
Time
UER
  : how soon will the first CE evolve to the first UER?
  : how much time remains to prevent crashes?
  : how long will the next UER occur once appearing a UER?
Time interval
  A significant probability that two successive UERs occur within one hour
  Bank may have encountered CEs long time ago

## Slide 12
Analyses: Impact of Power
Power trend before errors
  UER/CE peak/average power: the peak and average power of last ten minutes
  Average and peak power of server: the average of all recorded peak and average power
  The average and peak power both exhibit a rapid increase when approaching the error occurrence.
Notes: Traditional DRAM has reached its physical limits, making it challenging to further increase memory density and capacity.
The emerging NVM, such as Intel's Optane and Everspin's STT-RAM,
is considered a new way to break the scaling constraints of the main memory
due to its DRAM-comparable access performance and higher memory density.
However, as NVM density increases, it faces a significant problem of write disturbances
that impact the reliability of the memory system.

## Slide 13
Analyses
  Dataset overview (§3.1)
  Errors in HBM exhibit strong spatial locality. (§3.2)
  Servers that have experienced CE storms may increase the probability of encountering UERs (§3.3)
  The temperature distribution of CEs and UERs exhibits significant differences (§3.4)
  More details in the paper
Notes: Traditional DRAM has reached its physical limits, making it challenging to further increase memory density and capacity.
The emerging NVM, such as Intel's Optane and Everspin's STT-RAM,
is considered a new way to break the scaling constraints of the main memory
due to its DRAM-comparable access performance and higher memory density.
However, as NVM density increases, it faces a significant problem of write disturbances
that impact the reliability of the memory system.

## Slide 14
Outline
Background
Analyses and Findings
Calchas: Hierarchical Prediction Framework
Conclusion
Notes: I will introduce our work from these four parts.

## Slide 15
  The prediction methods used in tradiontional DRAM are not working in HBM.
Failed Attempts: CE-based Prediction
Is promise of using CE to predict upcoming UER in HBM?
  CE rate indicator[4]: consider a UER may occur when the number of CEs exceed the predefined threshold
  CE-based predictor[5]: utilize all the features related to CEs to predict future UER
  How to conduct a HBM-specific predictor to improve the prediction performance?
[4] Du et al. Predicting uncorrectable memory errors for proactive replacement: An empirical study on large-scale field data. Proc. of EDCC, 2020.
[5] Boixaderas et al. Cost-aware prediction of uncorrected dram errors in the field. Proc. of SC, 2020.
Notes: Xiaoming Du, Cong Li, Shen Zhou, Mao Ye, and Jing Li.
Predicting uncorrectable memory errors for proactive
replacement: An empirical study on large-scale field
data. In Proceedings of 2020 16th European Dependable Computing Conference (EDCC), 2020.

## Slide 16
Calchas: Design Guideline
Key factors for designing an efficient predictor
  Which features should be utilized to enhance prediction performance?
    Component features and statistical features?
  How can predictions be made to fully leverage the correlation between features and failures?
    Micro-level, HBM-level or server-level?
  When is the appropriate time to make predictions?
    Period-based or event-driven?
Notes: Traditional DRAM has reached its physical limits, making it challenging to further increase memory density and capacity.
The emerging NVM, such as Intel's Optane and Everspin's STT-RAM,
is considered a new way to break the scaling constraints of the main memory
due to its DRAM-comparable access performance and higher memory density.
However, as NVM density increases, it faces a significant problem of write disturbances
that impact the reliability of the memory system.

## Slide 17
Calchas: Feature Generation
Which features should be utilized to enhance prediction performance?
  Component features: number of components experiencing errors
  Stack features: one-hot code of SID positions
  Sensor features: variation of both power and temperature
  The 3D-stacked structure of HBM cause its characteristic (e.g., poor heat dissipation[6]) different from DRAM.
[6] Son et al. Thermal and Signal Integrity Co-Design and Verification of Embedded Cooling Structure With Thermal Transmission Line for High Bandwidth Memory Module. IEEE TCPMT, 1542-1556, 2022.
Notes: 第二张换成散热图

## Slide 18
Calchas: Hierarchical Prediction
  How can predictions be made to fully leverage the correlation between features and failures?
  Micro-level predictor: consider row-level, col-level, and bank-level prediction, respectively
  Server-level predictor: capturing the symptom of server failure
  Errors may occur along a row, a column, or across in a bank.
  Temperature is different before the UER occurrence.

## Slide 19
Calchas: Prediction Timing
Last prediction time
Time
Observation
window
Prediction
window
Last prediction time
Time
Prediction
window
Observation
window
When is the appropriate time to make predictions?
  Period-based approach: perform prediction every cycle
  Event-driven approach: prediction triggered by error events
UER
CE
No error
Benificial for regularly capturing the symptom
Server-level
predictor
Provide a rapid response to errors
Micro-level
predictor

## Slide 20
Calchas: Prediction Performance
Experimental Setup
  Ratio of train and test datasets: 70% vs 30% based on timestamp
  Metrics: Presion, recall, and F1-score
  Models: SVM, GBDT, and RF (sklearn v0.24.2)
  Based on RF, Calchas can achieve a highest precision of 58.0%, recall of 74.6%, and F1-score of 64.7% on average.
Notes: Traditional DRAM has reached its physical limits, making it challenging to further increase memory density and capacity.
The emerging NVM, such as Intel's Optane and Everspin's STT-RAM,
is considered a new way to break the scaling constraints of the main memory
due to its DRAM-comparable access performance and higher memory density.
However, as NVM density increases, it faces a significant problem of write disturbances
that impact the reliability of the memory system.

## Slide 21
Outline
Background
Analyses and Findings
Calchas: Hierarchical Prediction Framework
Conclusion
Notes: I will introduce our work from these four parts.

## Slide 22
Conlusion
Key Findings
  Lower SIDs (i.e., SID1) exhibit a higher susceptibility to errors
  Column-related error modes are prevalent in HBM
  Two successive UERs may occur within one hour
  Power increase when approaching the error occurrence
  ......
Our Solutions: Calchas
  Combines features specific to HBM with those used in traditional DRAM
  Employs both period-based and event-driven methods to realize the elastic and adaptive prediction
  More details in the paper
Notes: In conclusion, our findings indicate that block selection can reduce WD errors, but the selection process incurs high latency.
Further analysis reveals that reducing WD-prone writes can mitigate WD errors.
To address this, we propose LearnWD, which utilizes the two observations to classify the stale blocks and select a suitable cluster for new blocks.
LearnWD further utilizes MinHash to find the most similar stale block to the new block for overwritten to reduce RESET operations
and further decrease WD errors.
Experimental results demonstrate that LearnWD can assist existing encoding schemes in further reducing WD errors.

## Slide 23
Removing Obstacles before Breaking Through the Memory Wall:
A Close Look at HBM Errors in the Field
Thanks & QA
Contact Information: Ronglong Wu (rlwoo@stu.xmu.edu.cn)
26th ACM SIGOPS Chinasys Workshop
XMU ERAS Research Group: https://xmusys.github.io/
Contact email: Ronglong Wu, rlwoo@stu.xmu.edu.cn
Notes: That’all. Thank you.